## Slide 1: SNMP
SIMPLE NETWORK MANAGEMENT PROTOCOL

## Slide 2: NETWORK DEVICES:
SNMP-Compatible Network Devices
Routers
Switches
Firewalls
Wireless Access Points (APs)
Network Printers
IP Phones (VoIP devices)
Servers (Linux, Windows, etc.)
Network Storage Devices (NAS, SAN)
UPS (Uninterruptible Power Supply) systems
Environmental Monitoring Devices (e.g., temperature sensors)
Load Balancers
CCTV Cameras / IP Cameras
Modems and Gateways
VPN Appliances
Network Monitoring Probes

## Slide 3: SNMP ARCHITECTURE

## Slide 4: SNMP MANAGER (NMS)
NMS -> Network Management System (NMS)
A centralized system used to monitor, manage, and control network devices.
It communicates with SNMP Agents installed on devices.

## Slide 5: NMS
Sends SNMP requests (GET, GET-NEXT, SET) to agents
Receives SNMP traps and inform messages from agents
Collects and displays data from network devices
Alerts admins to events (e.g., link down, high CPU)
Analyzes performance and usage trends
Configures device settings via SNMP SET commands

## Slide 6: SNMP AGENT
Resides on network devices like routers, switches, servers, etc.
Collects and stores management information in a local MIB (Management Information Base)
Responds to SNMP requests (GET, GET-NEXT, SET) from the SNMP Manager
Sends SNMP traps or inform messages to notify the manager about significant events
Provides real-time status and performance data of the device
Acts as an interface between the device’s operating system and the SNMP Manager

## Slide 7: MIB (MANAGEMENT INFORMATION BASE)
MIB is like a database that stores information about network devices
SNMP uses MIB to get or set information on a device.
MIB treats network devices as objects.
A device is a collection of managed objects
Each object represents a specific piece of information about the device (e.g., interface status, IP address, CPU load).
MIB uses a tree structure
Related objects are grouped into table

## Slide 8: OID (Object Identifier)
It is a unique address or identifier used to locate a specific piece of information in a device’s MIB
It’s a unique numeric identifier assigned to each object in the MIB tree
Used by SNMP Managers to query or set values on network devices
Represented as a series of numbers separated by dots (e.g., 1.3.6.1.2.1.1.5.0)
Each OID corresponds to a specific object (e.g., system name, CPU usage, interface status)
OIDs are hierarchical, forming a tree structure defined by international standards (ISO, ITU-T, etc.)

## Slide 9: POLLING:
SNMP polling is the process where an NMS sends SNMP GET requests to a managed device to retrieve status and performance data from its MIB
Polling is done on a scheduled basis
It gives a real-time overview of device health
When the SNMP Manager asks for an OID, the agent replies with a pair: the OID and its current value.
The response contains both OID and the actual data.

## Slide 10: AGENT <--> MANAGER COMMUNICATION
Command | Sent By | Description
GET | Manager | Requests value of a specific OID.
GET-NEXT | Manager | Requests the next OID in the MIB tree.
GET-BULK | Manager | Retrieves large sets of data (SNMPv2+).
SET | Manager | Updates value of an OID on the agent.
RESPONSE | Agent | Reply to GET/SET with data or status.
TRAP | Agent | Sends alert/event notification to manager without GET request.
INFORM | Agent | Like TRAP, but expects acknowledgment.

## Slide 11: SNMP POLLING
Commands:
Snmpget
Snmpwalk
Snmp status

## Slide 12: Simulation 1:
Kali Linus as NMS
Localhost as snmp Agent
Polling between kali and localhost – list out the OIDs of localhost

## Slide 13: Simulation 2:
Kali as NMS
Windows as snmp agent
Will list out the OIDs of windows

## Slide 14: SNMP Versions:
V1:
SNMP v1/v2c/v3 differ in security, performance, and protocol features
UDP-based, runs on port 161 (for queries), 162 (for traps)
uses UDP, not TCP
GET, GET-NEXT, SET, TRAP
lacks support for bulk transfers or 64-bit counters

## Slide 15: V1 Limitations:
There is no security like encryption
TRAPS are available not INFORM, questions reliability
Bulk operations not possible
Limited Data Types
Poor error handling capacity
Outdated & Deprecated.

## Slide 16: SNMP V2c
Faster Performance with GETBULK
It can retrieve multiple variables in one request
SNMPv2 introduces Counter64 to handle high-speed interfaces
SNMPv2 adds more detailed and meaningful error codes
SNMPv2 supports INFORM messages
SNMPv2 introduced a more structured and consistent MIB module format

## Slide 17: Limitations of v2c
No encryption, no authentication, no access control
Anyone on the network can sniff or spoof SNMP traffic
completely insecure for sensitive environments
No User-Based Access Control
many agents and tools don’t support INFORM well
Not Suitable for Secure Environments

## Slide 18: SNMP v3
Enhanced version
Same protocol structure as v2c
Has security features
Verifies the identity of the SNMP user (e.g., using MD5 or SHA)
Protects data with encryption (e.g., DES, AES)
User-based Access Control
Prevents unauthorized monitoring or changes

## Slide 19: Limitations of NMS:
Limited to network devices, Can't monitor full infrastructure
Weak app monitoring, Misses server/service failures
Basic alerting, No custom rules or automation
Poor scalability, Can't handle large networks well

## Slide 20: Nagios XI
Nagios XI is an enterprise-class IT infrastructure monitoring and alerting platform developed by Nagios Enterprises
Monitors entire IT infrastructure — network devices, servers, applications, and services
Highly customizable — supports thousands of plugins and custom checks
Flexible alerting system — email, SMS, Slack, webhooks, and more
Supports SNMP polling and traps — ideal for both active and passive monitoring
Automated actions via event handlers — can auto-restart services or run scripts
Strong community and documentation — well-supported and widely adopted

## Slide 21: SNMP with Nagios XI
SNMPTT : SNMP Trap Translator
It is a daemon or script written in Perl
It receives SNMP traps
Translates OIDs (Object Identifiers) into readable descriptions using MIB files.
Logs messages in various formats (e.g., syslog, text file, database).
Can execute programs or scripts based on specific traps.